Pump Performance

Procedure

- Control Station ON.

- Log on computer.

- Edibon Menu

- Insert large weir.

- Open Centrifugal pump valve fully; close gear pump valve completely.

- Select Centrifugal Pump.

- Select f drive.  Centrifugal Data file; OK to replace existing file.

- Set Actuator to ~ 3000rpm.  Allow ~ 60s to stabilize flow.

- Select Table

- Select Average, then Acquire.

- Repeat for five additional pump speeds.

- STOP, the QUIT.

- Go to Computer; select f drive.  View data table “Centrifugal.DAT”

- Use data table to plot performance curves: head, efficiency, and power vs flow.

- CAUTION:  B	E SURE YOU HAVE SAVED THE CENTRIFUGAL PUMP DATA BEFORE YOU START THE GEAR PUMP TRIAL.  The computer may overwrite gear data over the centrifugal data.

- Close Centrifugal pump valve completely; open gear pump valve completely.

- Insert small weir.

- Repeat the experiment for the Gear pump.  Do not exceed 450rpm

- Prepare performance curves for the gear pump.

Report

- Plot pump head and efficiency vs pump discharge for centrifugal pump.

- Plot pump head and efficiency vs pump discharge for gear pump.

- Use the first set of data for the centrifugal pump ONLY.

  - Calculate the pump head from the data.

  - Calculate the pump power from the data.

  - Calculate the mechanical power of the pump.

  - Calculate the pump efficiency based on the mechanical power.