## Slide 1: IT 4833
Cellular Security
Created by: Dr. Lei Li and Professor Darin Morrow

## Slide 2: Road Map
Introduction
Security Auditing & Risk Analysis
Evolution of Wireless Network
WLAN
Security
WLAN
Overview
WLAN Threats
& Vulnerabilities
Infor. Security
Essentials
WLAN
Security
WLAN
Security Tools
Mobile
Security
Mobile Network
Overview
Cellular Network
Security
Mobile Security
Threats
Mobile Devices
Security

## Slide 3: Learning Outcomes
After this module, a student will be able to:
Describe the security vulnerabilities present in 1G TWN
Describe the security architecture of GSM
Describe the existing issues in GSM security
Discuss the security improvement of 3G and 4G LTE network comparing to GSM
Describe the security features of UMTS (3G) and LTE (4G)
Briefly describe Network Access Security and Network Domain Security.
Discuss the l attacks on 3G and 4G network

## Slide 4: 1G Cellular Network
No Security
Electronic Serial Number (ESN) cloning

## Slide 5: 2G Cellular Network (GSM)
https://www.sans.org/reading-room/whitepapers/telephone/gsm-standard-an-overview-security-317

## Slide 6: GSM Security Functions
Authentication of the registered subscribers only
Secure data transfer through the use of encryption
Mobile phones are inoperable without a SIM
Duplicate SIMs are not allowed on the network
Securely stored KI

## Slide 7: GSM - Authentication
https://www.sans.org/reading-room/whitepapers/telephone/gsm-standard-an-overview-security-317

## Slide 8: GSM- Anonymity
International Mobile Subscriber Identity (IMSI)
Temporary Mobile Subscriber Identity (TMSI)
IMSI is rarely transmitted after authentication unless it’s absolutely necessary

## Slide 9: GSM – Encryption & Decryption
Authentication Algorithm A3
Ciphering Algorithm A5
Ciphering Key Generating Algorithm A8

## Slide 10: GSM Security Challenges
Unilateral authentication and vulnerability to the man-in-the-middle attack
Flaws in implementation of A3/A8 algorithms
SIM card cloning
Over-the-air cracking
Flaws in cryptographic algorithms
Etc.

## Slide 11: 3G (UTMS) Security Improvement
The extension of encryption and integrity protection
Protection of the signaling infrastructure in the core
network
The cryptographic keys derived on the User Services
Identity Module (USIM) are longer in UMTS (128-bits)
than in GSM (64-bits).
Standard encryption algorithms used by 3G were openly published.
The definition of standard UMTS authentication algorithms

## Slide 12: 3G/LTE Security Architecture
Image source: https://www.researchgate.net/publication/235339185_Security_of_3G_and_LTE

## Slide 13: 3G & 4G Security Features
Network access security (NAS)
Network domain security (NDS)
User domain security (UDS)
Application domain security (ADS)
Visibility and configurability of security

## Slide 14: 4G LTE Security Improvement
An extended key hierarchy
Use even longer cryptographic keys
(256-bits) and the inclusion of better cryptographic ciphers.
Separation of control plane and user plane
Integrated inter-working security for legacy and non-
3GPP networks.
Greater protection for back-haul link since the physical
security of an eNB cannot be trusted.
Mutual authentication between a relay node and the network.
Requiring the use of the USIM and excluding the GSM SIM.

## Slide 15: 5G
5G is the fifth generation of cellular network technology, introduced as the successor to 4G. It offers significant improvements in speed, latency, and connectivity, enabling a wide range of advanced applications. Here are some key points about 5G:
Speed: 5G can achieve peak download speeds of up to 10 Gbps, significantly faster than 4G1.
Latency: It has ultra-low latency, often around 1 millisecond, which is crucial for real-time applications like remote surgery and autonomous vehicles1.
Capacity: 5G networks can support a much higher number of connected devices simultaneously, making it ideal for the Internet of Things (IoT) and smart cities1.
Technology: It uses advanced technologies like Massive MIMO (Multiple Input Multiple Output), beamforming, and network slicing to enhance performance and efficiency
Use Cases: 5G enables new applications such as extended reality (XR), industrial automation, and enhanced mobile broadband1.
Challenges: Despite its benefits, 5G deployment faces challenges like significant infrastructure investment, spectrum allocation, and security concerns1.

## Slide 16: Network Access Security
User identity confidentiality: Ensuring that a user's identity information remains private and protected from unauthorized access
Entity authentication and key agreement: A security process where entities (e.g., devices or users) verify each other's identities and establish shared cryptographic keys for secure communication
Data confidentiality and integrity: Ensuring that data is accessible only to authorized users (confidentiality) and remains accurate and unaltered (integrity) during storage and transmission

## Slide 17: Network Domain Security
Security of the communication between network nodes, located either in the same or in different networks
Protect the core network signaling protocols
  confidentiality, integrity, authentication and anti-replay protection
  Standard procedures based on cryptographic techniques

## Slide 18: Cyber Attacks to 3G & LTE
Crypto-attack
Denial of Service attack
Side-channel attack

## Slide 19: Reference
https://books.google.com/books?id=IHg0JBShDhEC&pg=PA369&lpg=PA369&dq=security+in+first+generation+traditional+wireless+networks&source=bl&ots=l41aXRqaZG&sig=oovVfZ5rO0fHByWNvBH2gxi1eG4&hl=en&sa=X&ved=0ahUKEwj3ysn71-rUAhXLdj4KHc9lBI8Q6AEIMTAC#v=onepage&q=security%20in%20first%20generation%20traditional%20wireless%20networks&f=false
https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=web&cd=4&ved=0ahUKEwjz6t612-rUAhXHzz4KHV7FAksQFghBMAM&url=https%3A%2F%2Fwww.sans.org%2Freading-room%2Fwhitepapers%2Ftelephone%2Fgsm-standard-an-overview-security-317&usg=AFQjCNEVQqhFN991Ei5NxPmDY5V_wCnSiA&cad=rja (
https://arxiv.org/pdf/1002.3175.pdf
https://www.researchgate.net/publication/235339185_Security_of_3G_and_LTE
https://www.researchgate.net/publication/235339185_Security_of_3G_and_LTE https://www.researchgate.net/publication/235339185_Security_of_3G_and_LTE https://www.researchgate.net/publication/235339185_Security_of_3G_and_LTE