Fluid Mechanics Lab

MET 3344

Open Channel Flow

Procedure:

- Measure the length, width, and slope of the upper section of the flume.

- Start the pump and allow flow to stabilize.  Start with flow valve wide open.  Record the flow meter reading.

- Record the depth of flow for the Manning calculation.

- Install a weir plate; allow the flow to stabilize.  Measure appropriate dimensions (L & Hc).  Use rectangular weir plates.

- Record the depth of flow upstream of the weir at a distance of at least 4Hmax.

- Install the V-notch weir plate and repeat Steps 4 & 5.  No L value is needed.

- Repeat these steps (4 through 7) for an additional flow valve settings.

Report:  For each flow valve setting:

- Use the appropriate weir equation and calculate the flow rate in cfs; convert to gpm.  Example:  for contracted rectangular weir Q = 3.33 LH3/2 (cfs).  Refer to Mott p. 463 or Cengel p. 720.

For 60o weir plates  Q = 1.43 H5/2 (cfs); convert to gpm.

2.  Calculate the volumetric flow in gpm from the

Manning equation.  Q = (a/n) A Rh2/3So1/2.  Determine

n from tables in text.

3.  In Conclusions, compare the three values for agreement at each

flow valve setting: rectangular weir, 60o weir, and

Manning Equation.  Compare to the flow meter

Readings; assume the flow meter is providing “true” flow measurements.